## Slide 1
River Watch and the published station network
DHM discussion draft · 21 September 2026
01
447
450
604.5
647
670
684
River Watch via BIPAD
112 PDF stations
Six delivered series
NEPAL
Published stations with delivered history
447 Trisuli · Betrawati
450 Narayani · Devghat
604.5 Arun · Turkeghat
647 Tamakoshi · Busti
670 Dudhkoshi · Rabuwa Bazar
684 Tamor · Majhitar
For DHM to confirm
Which sites share automatic and manual records?
Which official station IDs link history to the live feed?
Matching names appear in River Watch for all six. Site identity and datum still need confirmation.
Notes: Sources: DHM Updated_Published_Station_List_2023.pdf, all 3 pages, internally marked updated July 2025. All 112 coordinates transcribed directly from scan. River Watch layer: https://bipadportal.gov.np/api/v1/river-stations/?limit=500 retrieved 21 September 2026, 284 metadata rows. 283 entries have coordinates in the Nepal map extent. One record, Roshi Khola at Kavre (API ID 270), has apparently reversed coordinates and is omitted without guessing a correction. These are catalogue entries, not a count of working sensors; freshness varies. DHM public page: https://www.dhm.gov.np/hydrology/river-watch . BIPAD attributes these records to DHM. Boundary: local geoBoundaries NPL ADM0 simplified, https://www.geoboundaries.org/ . Map uses longitude/latitude with longitude scaled for Nepal. Symbols indicate source membership, not station technology or rating availability. PDF and portal locations can differ. PDF coordinates take precedence for highlighted stations per project decision. Matching names do not prove common instrument, datum or time-series continuity. API IDs of candidate matches: 137,25,37,61,89,63 respectively for 447,450,604.5,647,670,684. Full operational crosswalk requires DHM confirmation. Ask DHM to annotate whether each site has telemetry, staff readings, discharge gaugings and currently usable ratings. Public River Watch warning display does not imply warning-only use or absence of ratings.

## Slide 2
What each instrument measures and where the data goes
DHM discussion draft · 21 September 2026
02
Conceptual station cross-section. Equipment and reporting paths vary by site.
Automatic level sensor
Water level h(t), metres
Logger and telemetry
Manual staff gauge
Observer reads h(t)
Same gauge zero?
Discharge gauging visit
Velocity + area give Q (m³/s)
Paired h and Q support a rating table
h + a valid rating table = estimated Q
Telemetry database / API
Water levels
River Watch and warning checks
Manual records: where?
Observer log / regional office / HQ?
Entry time and transfer lag?
Hydrological archive
Gaugings and rating versions
Historical discharge publication
telemetry
reporting?
Same database? API access? Lag?
Notes: This is an editable conceptual diagram, not a surveyed DHM station or a confirmed DHM database architecture. Automatic sensors and manual staff gauges both measure stage; periodic velocity-area or ADCP discharge gaugings are a different observation. The same site may host all three. A radar-style sensor appears here illustratively; DHM must confirm installed sensor type. General measurement reference: USGS, https://www.usgs.gov/water-science-school/science/how-streamflow-measured . DHM source questions: docs/requirements/dhm-data-formats-questions.md, sections 1, 3, 4, 5, 7. Ask: (1) Does the observer read at fixed times, and which times? (2) Paper, phone, SMS, app or direct entry? (3) Who enters and checks the data? (4) Where are manual stage readings and discharge gaugings stored? (5) Same DMS as telemetry or a separate archive? (6) Do provisional manual values reach headquarters and our interface before the forecasting cutoff? Record typical delay, worst delay, weekends and monsoon disruptions. (7) Do manual and automatic gauges share a zero and correction history? (8) How often are discharge gaugings done, especially after channel changes? (9) Who signs off and distributes new rating versions? The boxes depict logical data holdings; their physical separation is deliberately unresolved. Existing notes record no current rating tables for the six delivery stations (Plan 268 D8). Do not extrapolate historical ratings silently.

## Slide 3
Historical inputs and the missing operational feed
DHM discussion draft · 21 September 2026
03
HISTORICAL FILES
DHM discharge delivery
DFL_447.txt … DFL_684.txt
Comma-separated daily Q records
Six stations, with historical RT files
Dudh Koshi water-level CSV
Water Level Inst … 2025-11-21.csv
Columns: dateTime (NPT), value (m)
Historical CSV / file preparation
Training and hindcasts
Units, dates, QC and daily
aggregation must agree
Forecast tools
Historical model fitting
Operational forecasts need
a timely, compatible input feed
OPERATIONAL SOURCES
DHM operational database
Automatic water levels
Manual entries also included?
Manual / hydrological archive?
Staff readings and discharge gaugings
Where stored, and how late?
?
Which feed can supply
the forecast run on time?
Recorded gap: no current rating tables for the six sites. Is approved provisional Q available?
Notes: Historical source files inspected in the local BARHKH data/runoff directory. DFL_{447,450,604.5,647,670,684}.txt and RT files are the September 2026 delivery. DFL files are text with comma-separated date/discharge records, not literal .csv filenames. Separate historical file: DHM_subdaily_DudhKoshi/Water Level Inst from 2014-01-01 to 2025-11-21.csv; header inspected: dateTime (NPT), value (m). Filename denotes requested range, not verified complete coverage. Its provenance note credits Binod Parajuli / DHM, shared by Silvan Ragettli November 2025, and marks measurements confidential. No measurement values are reproduced. Historical CSV preparation and ingestion into forecast tools are the user's described workflow; this deck does not assert that all six September files have completed ingestion in SAPPHIRE Flow. Plan 268 remains DRAFT. Source: docs/plans/268-dhm-barkhk-runoff-delivery.md, especially D8: owner-recorded position is that current rating tables do not exist for these stations. Ask whether that position has changed, whether DHM provides an approved provisional Q product, or whether a level-based forecast / model without recent Q is the agreed interim scope. Do not apply expired ratings by default.
API development is no longer an unknown format: docs/requirements/dhm-api-examples/README.md and Plan 300 record provider confirmation, relayed by owner 16 September, of the BIPAD/DHM request-response contract, and completed offline adapter implementation. Direct DHM base URL, credentials, activation, station crosswalk, datum, history coverage, latency and QC/correction semantics remain unresolved. The large question mark concerns delivery and scientific suitability, not whether an API parser can be built.
Meeting decisions: Choose h or Q for each model input and forecast target. Obtain a per-station manifest linking official ID, API station/series ID, instrument, datum, current status, observation interval, last usable timestamp, available history and owner. Specify the forecast issue time in NPT, latest required observation, usual/worst arrival lag, and missing-data fallback. Distinguish manual observation time, reporting time, entry time, QC release and API visibility. Determine whether the public display, telemetry database and hydrological archive expose the same measurements, including manual readings. Identify an approved Q source or new-rating delivery date. Agree history/operations overlap testing, local-day definition, aggregation method, provisional/final status, correction handling and backfill. Ask DHM to demonstrate one automatic and one manual record end to end. Assign each unresolved answer a named owner and date. Weather observations and forecasts are separate model inputs outside this river-data discussion.